## Slide 1: Micro-Architecture
Chapter 4
Implementing the Instruction Set Architecture

## Slide 2: Example Integer Java Virtual Machine
Micro-program has simple instructions and state (values assigned to variables)
State changes as code executes
Machine runs in a fetch-execute loop
  Fetches instruction (opcode =operation code)
  Fetches operands (data)
  Executes

## Slide 3: Data Path
Part of the CPU containing ALU, its inputs and outputs
Some registers have symbolic names MAR, MDR, PC etc

## Slide 4: Notation
Registers can write data into gray B bus
C bus writes data into registers
Light arrows exchange data with memory

## Slide 5: Operation
Operands to ALU come from register H and bus B
Note: H is written as output from Shifter
Six control lines for ALU, one for Shift control

## Slide 6: Control Signals to ALU
ENA, ENB –enable A, B
INVA –invert A,
INC – increase by 1
Can load ALU, pass the data through Shifter and store it in H in the same cycle.

## Slide 7: Data Path Timing
Have four sub-cycles in a clock cycle
  Control signal setup
  Load register
  ALU shift op
  Result back to registers along C bus

## Slide 8: Data Path Timing
Starts with falling edge of clock
Ends with rising edge of clock

## Slide 9: Memory Operation
Have 32 bit word-addressable port and 8 bit byte addressable port (controlled by PC)
MAR, MBR PC are registers
MBR can only output data to bus B in two formats

## Slide 10: Memory Operation
MBR, MAR, PC driven by control signals
MAR, H does not have enable signals -always on
MAR has word addresses, PC has byte addresses
Resulting memory fetch will be put into low order 8 bits of MBR
PC/MBR is used to read instructions (executable byte stream). All,other registers use words
MAR/MDR used to read operands (word boundary)
Output of MBR gated to bus B

## Slide 11: Output Formats of MDR
8-bit Unsigned Values:
  Used for indexes or part of 16 bit integers
  Put into low 8 bits in bus B
  Zeros in upper 24 bits
Signed value between –127 and +127:
  Copy MBR sign bit (leftmost 8) into 24 leftmost bits
  Put numerical value into 8 rightmost bits
  (known as signed extension)
  That is why there are two lines from MBR to B

## Slide 12: Need 29 Signals
9 to write from C bus
9 to write to B bus
8 to control ALU and shifters
2 to indicate r/w to MAR/MDR
1 for memory fetch via PC/MBR

## Slide 13: Microinstructions
Cycle =
  Gating values on to B
  Propagating values through ALU and shifters
  Driving signals on to C bus
  Writing results in registers
  If memory r/w asserted, initiate action
Memory operation started at end of cycle
Data available only after next cycle. (one cycle missed!)
May write value in C onto more than one register, but never put value onto B from more than one register

## Slide 14: Microinstruction Formats
To select inputs to B bus need 4 bytes (2**4=16)
Bits needed for controlling data path = 9+4+8+2+1 = 24 bits for one cycle
NEXT_ADDRESS and JAM needed to indicate next instruction to be fetched

## Slide 15: Microinstruction Formats
Addr: potential next address
JAM how next microinstruction is selected
C: Which register written from C
Mem: memory function
B: Source of B

## Slide 16: Microinstruction Control
Sequencer steps through operations to execute each ISA instruction providing
  State of each control signal (asserted or not)
  Address of next instruction
Control Store = holds microprogram, made of read only memory (logic gates)
Example control store contain 512, 36 bit words
Each microinstruction specifies its successor
Needs own
  counter = MPC (Microprogram counter)
  Memory data register = MIR (Microinstruction register)

## Slide 18: MPC, MIR
4 B bits drives 4 to16 decoder for bus B
Steps:
  At falling edge MIR loaded from word in control store pointed by MPC (s-Cycle 1)
  Signals propagate to data paths and register put onto bus B
  ALU knows operation (s-Cycle 2)

## Slide 19: MPC, MIR
Steps:
  ALU, N, Z stable output in s-Cycle 3
  Output propagates to register via C bus
  Registers, N, Z loaded in s-Cycle 4

## Slide 20: Determining Next Instruction
Starts when MIR is stable
NEXT-ADDRESS copied to MPC
  If JAM is 000 nothing more done
Else
  If JAMN is set N is ORed to higher order bit of MPC
  If JAMZ is set Z is ORed to higher order bit of MPC
Why?
  Because after rising edge of clock bus B outputs no longer valid: ALU outputs not reliable, hence save status in N and Z

## Slide 21: Determining Next Instruction
High Bit set
Boolean Function Computed in Logic Gate =
  (JAMZ) or
  (JAMN and N) or
  NEXT_ADDRESS[8]
MPC takes either of:
  NEXT_ADDRESS
  NEXT_ADDRESS with higher order bits ORed

## Slide 22: Determining Next Instruction: Example
Current Instruction @ 0x75 has NEXT_ADDRESS = 0X92.
  If Z bit is 0, next instruction = 0x92, else 0x192

## Slide 23: Using MBR for Next Address Computation
If JMPC set, 8 MBR bits bitwise Ored with 8 low order bits of NEXT_ADDRESS field
When JMPC is 1, 8 low order bits of NEXT_ADDRESS is zero, higher order is 0 or 1
So NEXT_ADDRESS becomes 0x000 or 0x100
Allows multi-way branching (jump), MBR has opcode

## Slide 24: How Microinstructions Work: Summary
SubCycle 1: MIR loaded from address in MPC
SubCycle 2: MIR propagated out, B loaded
SubCycle 3: ALU, Shifter produce stable value
SubCycle 4: C, Memory and ALU stable
  Registers loaded from C
  N, Z loaded
  MBR, MDR get values from memory (If started in previous cycle)
  MPC gets value
New cycle begins

## Slide 25: An Example ISA: IJVM
Stacks: Used to implement procedures
Stack frames are used to store store:
  local variables (environment)
  Temporary results of arithmetic computations
LV bottom, SP top of stack.
  Base+offset addressing

## Slide 26: Stacks for Arithmetic
Stacks are rarely used for arithmetic operations
Could be mixed in with local variable stack

## Slide 27: The Memory Model
Memory = 4GB = 1 GB array of 4 byte words
4 Separate areas:
  Constant Pools:
    Contain constants, strings, and pointers to other areas
    Cannot be written by an IJVM program.
    Loaded when program is bought into memory
    CPP is the beginning address
  Local Variables
    For each method (function, procedure) there is a frame
    Beginning has (in and out) parameters
    LV is the beginning of Local Variable stack

## Slide 28: IJVM Memory Model - Cont
  Operand Stack
    Of constant size, computed at compile time
    Directly above LV stack.
    SP indicate end
  Method Area
    Text area of code reside here
    PC points to an address here containing the next instruction to be fetched.
All addresses refer to words (4 byte)
  Eg: LV+4 refers to 4th word after L.

## Slide 29: IJVM Memory Model

## Slide 30: IJVM Instruction Set
Instructions consists of an opcode and optional parameters, encoded in Hex
Instructions work as:
  Push words onto stack from various sources
    Constant pool: LDC_W
    Local variable frame: ILOAD
    Instruction set: BIPUSH
  Compute
  Pop words and store in local variable frame ISTORE

## Slide 31: IJVM Instruction set

## Slide 32: IJVM Instructions
Some instructions come in various forms:
  Long general format
  Frequently used short format
Two Arithmetic operations:
  IADD, ISUB
Two Logical Operations:
  IAND, IOR
4 Branch Operations: offset follows opcode
  GOTO, IFEQ, IFLT, IF_ICMPEQ

## Slide 33: Call and Return Instructions
INVOKEVIRTUAL
  Invokes another method
  Caller pushes calee address onto stack OBJREF
  Caller pushes in parameters onto stack
  INVOKEVIRTUAL executed
IRETURN
  Returns to calee

## Slide 34: INVOKEVIRTUAL

## Slide 35: Format of Method
First word in method has special data
First two bytes
  Have # of parameters, with OBJREF counted as parameter 0
  LV points to OBJREF (parameter 0)
Last two bytes
  Size of local variable area of the method
  Needed to allocate stack for new call
Finally 5th byte has first opcode

## Slide 36: INVOKEVIRTUAL Execution
Compute address of OBJREF in constant pool using first two bytes
Compute base address of new stack # parameters from from stack size
Set LV to OBJREF. Now erase value there and put address at end of stack (increase by size of stack)
At this location put old PC, next put Callers LV, and reset SP to this address
Set PC to 5th byte in method code

## Slide 37: IRETURN

## Slide 38: Executing IRETURN
De allocate space
Overwrite OBJREF with return value
Use link pointer to restore LV and PC of the calee
In the next cycle, go back to instruction after the call in calee.
No explicit I/O, they are done by methods (I.e. no command line arguments)

## Slide 39: Compiling JAVA to IJVM

## Slide 40: Compiling JAVA to IJVM: Stack
Horizontal line: empty stack

## Slide 41: Implementing IJVM
Use Higher level syntax to indicate operations
Example: MDR = H+SP
  Load SP to B
  Load H and B to ALU and add them
  Store the result back in MDR
Be Careful: MDR = SP+MDR not legal
So is H=H-MDR as subtranhend must be in H
Memory read write indicated by rd, wr, WSP
Reads and writes happen in 4 byte words through 4-byte words
Opcode instruction fetch indicated by fetch

## Slide 42: Legal Instructions

## Slide 43: Microinstructions: Addressing
Each instruction explicitly supplies the next instruction’s address
Explicit jumps given by GOTO Label
Syntax for setting the JAMZ bit is
  If (Z) goto L1; else goto L2
Notation to set JMPC bit
  Goto(MBR OR Value)
Figure 4-17 gives the micro code with 112 instructions

## Slide 44: Part of Fig 4-17

## Slide 45: Microinstruction: Execution
Registers
  TOS: cache for SP
  OPC: temporary register
Has main loop to run the
  fetch-decode-execute cycle
At the beginning of each instruction
  PC loaded
  Opcode fetched into MBR
Please go through the instructions in 4.3.2

## Slide 46: Tradeoffs in Implementation
Speed vs. Simplicity
  Simple machines are slow and fast machines are complex
Cost measured in terms of area and not #of transistors any more.
Ways to make faster machines
  Make clock cycle shorter (I.e reducing execution path length)
  Instruction pipelining

## Slide 47: Reducing Execution Path Length
Merge interpreter loop with microcode
  When ALU not used in POP2, use it

## Slide 48: Reducing Execution Path Length
Have two input buses, A and B: Can add any two registers in one cycle

## Slide 49: Reducing Execution Path: IFU
Execution Loop
  PC passed through ALU and incremented
  PC used to fetch next byte of instruction
  Operands read from memory
  Operands written to memory
  ALU compute and store result
ALU intervenes in instruction fetching
  Have a separate Instruction Fetch Unit to
    Increment PC
    Fetch Bytes
    Assemble operands

## Slide 50: Instruction Fetch Unit
Two ways:
  IFU interpret code, fetch additional fields and assemble in register for execution
  Always fetch next 8- or 16- bytes regardless of use
  Second design shown
Use 2 MBR’s. (MBR1 holds oldest, and MBR2 two oldest bytes)
  Automatically senses when MBR1 is read
  Read next byte into MBR1
  When MBR1 is read, shift register shifts I Byte R
  When MBR2 is read it is loaded 2 bytes

## Slide 51: An Instruction Fetch Unit

## Slide 52: The Whole design

## Slide 53: Instruction Pipelining
Major components of the data path cycle
  Driving selected registers onto A and B
  ALU and shifter work
  Results get back to registers and stored
Can introduce latches to partition buses
  Parts operate independently
  Why
    Can speed up clock because maximum delay is less
    Can use parts during every sub cycle

## Slide 54: Latched
Each subcycle is about 1/3 original length
Previously during 1, 3 subcycles ALU is idle.
Now we can use it

## Slide 55: Pipelining: SWAP in Old Design
In new design, need 3 microsteps:
  Load A and B
  Perform operation and load C
  Write result back

## Slide 56: Implementing SWAP

## Slide 57: Dependencies
Like to start SWAP3 in cycle 3, but data available only in cycle 5.
I.e. : Instruction waiting for results of previous instruction, called
  True dependency, Read After Write dependency
Mic-3 requires 11 cycle times, Earlier one 9without pipelining takes 18 cycles.
Read Section 4.4.5: A seven stage pipeline

## Slide 59: Improving Performance
Ways to improve performance
  Modify implementation without architectural changes
    Can use same code, Major selling point
    80386 through Pentiums improvements are like this
Architectural changes
  New instruction sets
    RISC
Major Techniques
  Cache
  Branch prediction
  Out of order execution with register renaming
  Speculative execution

## Slide 60: Cache Memory
Split cache: Separate caches for instructions and data
  Two separate memory ports
  Doubles the speed with independent access
Level 2 cache: extra cache for instructions and data

## Slide 61: Cache
Caches are generally inclusive
  L3 caches include L2 caches and L2 caches include L1 caches
Depends on Locality of reference
  Spatial
  Temporal
Cache Model
  Main memory divided into fixed size blocks called caches lines – 4 to 64 consecutive bytes
If memory referenced,
  cache controller checks if included in caches,
  else a line is removed and new line cached

## Slide 62: Direct Mapped Caches
Given memory word stored exactly in one place
  If not there, not in cache
Format:
  VALID BIT: on if data valid
  TAG: (16 bit) value identifying line in memory
  DATA: (32 bytes) copy of data from memory

## Slide 63: Address Translation
TAG: Tag bit in memory
LINE: which cache entry holds data, if there
WORD: which word within line
BYTE: which byte with word (not used normally)
When CPU gives address, HW extracts LINE bits
  Indexes into cache, finds one of 2048 entries, if valid TAG field are compared, If same cache HIT!
  Else cache miss!, whole cache line fetched from memory, stored in cache, existing line stored back in necessary

## Slide 64: Performance: Direct Mapped Caches
Consecutive memory in consecutive cache lines/entries
If access pattern is precisely the size of cache, each access results in miss
Most common, collisions are rare

## Slide 65: N-way Set Associative Caches
Allow n-possible entry for each line
Each entry must be checked to see if needed line is present
2-way and 4-way caches have performed well

## Slide 66: Issues in Cache Design
Cache replacement policy: LRU, MRU
  Can change granularity of replacement
  Gives more slots for a data line
Writing Cache Back
  Write through
  Write deferred
Writing entry not in cache:
  Write Allocation: Bring to cache
  Write memory directly

## Slide 67: Branch Prediction
Pipelining is works best with liner code, but code has branches, hence branch prediction important
Most pipelined machines execute instruction following branch, logically should not do so
  Compilers can stuff No Op instructions, but slows down and makes code longer
Example Predictions
  All backward branches will be chose
  Forward branch taken when errors occur
Two ways of branch prediction
  Execute until change state (I.e write register) update scratch
  Record update value to be able to rollback in case of need

## Slide 68: Dynamic Branch Prediction
CPU maintains history table in HW.
  Look up history table for predictions
Organized just like caches
  Loop ends take wrong guesses, and messes up re-entry
    Hence change branch only after two correct executions
    Can take a Finite State Machine approach

## Slide 69: Static Branch Prediction
Compiler passed hints
  Sets a bit to indicate which branch will be mostly taken
  Requires special hardware (enhanced instructions)
Profiling
  Program run though a profiler (simulator ) to collect predictions, and pass them to the compiler
  Limited use

## Slide 70: Out of Order Execution
Pipelined superscalar machines fetches and issues instructions before they are needed
Inorder issue and retirements is simpler but waste time.
Some instructions depend on others, hence cannot resort to out of order execution.
Example machine:
  8 registers, 2 for operands, one for result
  Decoded in cycle N execution starts in N+1
  Addition subtraction written back in N+2
  Multiplication written back in N+3
Scoreboard for use of registers for reading and writing

## Slide 72: Example: In order execution
In order issue and in order retirement
  Needed to keep precise interrupt
    Up to some instruction completed, all beyond not
Instruction Dependencies
  RAW: If any operand being written, do not issue
  WAR: If result register being read, do not issue
  WAW: In result register being written, do not issue
I4 has RAW dependency, stalls
  Decode units stalls until R4 available
  Stops pulling from fetch unit
  When buffer full fetch unit stalls fetching from memory

## Slide 73: Out of Order Execution
Issued out of order and may retire out of order
I5 issued without even when I4 is stalled
Problem: I5 can use an operand I4 computed
New Rule: Do not issue instructions that uses operand stored by previous instruction
Example: I7 uses R1, written by I6,
  never uses again because I8 writes R1,
  hence I6 can use different register to hold value
Register renaming: decode unit changes R1 in I6, I7 to S1 (secret) S1 so I5, I6 can be issued concurrently
Eliminates WAW and WAR dependencies often

## Slide 74: Speculative Execution
Code consists of basic blocks with no control structures such as if then else or while. Only linear sequence of code. No branches.
Within each block, reordering works well.
Program can be represented as a directed graph.
Problem: blocks are short, waste cycles
If slow instructions can be moved up across blocks, , so that if they are executed, then the result is there !
Speculative execution: execute code before known if they will be executed

## Slide 75
Speculative Execution: Example

## Slide 76: Speculative Execution: problems
In the example,
  say except even-sum and odd-sum kept in registers.
  Can move LOAD to top of loop.
  Only one of even-sum, odd-sum will be needed
All results must have no irrevocable results
Can rename all destination registers in speculative code
Problem: Speculative code causing exceptions
Solution: Use SPECULATIVE-LOAD instead of load so that in case of cache miss does not cause overload
Poison Bit: If causes trap in speculative code does not make it, instead sets bit, if register touched by regular one causes trap